## Slide 1: Introduction to Image Analysis with FIJI
Gayathri Nadar, Noreen Walker
Scientific Computing Facility, MPI-CBG
3.-7.5.2021
1. Introduction, Basic Concepts, Counting Objects
Topics:
Introduction to Image Analysis
What is an image
Introduction to FIJI
ROI and measurements
Counting objects (spot detection)
With material from:
Robert Haase
Benoit Lombardot

## Slide 2: Who are we?
André Gohr
Bioinformatician
Joining in 2021
Bioinformatics Data Analyst
RESEARCH DATA MANAGEMENT
& ELN SUPPORT
Stephan Janosch
Research Software Engineer
FACILITY LEADER
Lena Hersemann
Facility Leader
“The Scientific Computing Facility aims to provide a unified service to assist researchers in the tackling of scientific questions involving computational analysis, large data handling and image processing.”
Notes: Bio Image informatics service is embedded in the SCF:
Together with bioInformatics and Scientific software development

## Slide 3: Course Overview
Day 1 (Mon 3.5.)
  Image basics, visualization, measurements
  Spot detection
  Segmentation (start)
Day 2 (Tue 4.5.)
  Visit LMF
  Segmentation (cont’d)
  Mathematical background: image filters, morphology
Day 3 (Wed 5.5.)
  Advanced segmentation: Machine learning with Ilastik
  IJ Macro (start)
Day 4 (Thu 6.5.)
  IJ Macro (cont’d)
  3D data: visualization and analysis
Day 5 (Fri 7.5.)
  Image registration, image stitching
  Time sequence analysis and tracking
  Good practices
Notes: Course structure: afternoon session with 1 break in between
Slides + Demo + independent Exercises

## Slide 4: Overview
What is image analysis?
What is an image?
Tools for image analysis
Introduction to FIJI: image characteristics and visualization
ROIs and measurements
Counting objects: maxima detection
Notes: Overview course structure: presentations, demos (hands-on), and DIY exercises
Red and green post-its

## Slide 5: What is Bio-Image Analysis?
Segmentation
Bio-Image analysis
Tracking
Colocalization
Spot detection
Stitching
Image Correction

## Slide 6: Bio-Image Analysis
Image preparation
Find objects (segmentation)
Measurements
Example steps
Automation

## Slide 7: Bio-Image Analysis
Image preparation
Find objects (segmentation)
Measurements
Example steps
Automation
Goal of bio-image analysis:
Quantify image data objectively and reproducibly.

## Slide 8
What is an image?

## Slide 9: What is a digital image?
A digital image is a matrix with numbers.
A single pixel is the representation of one number of the matrix.
  A pixel is not a little square but just the visualization of a single number.
Images are characterized by size, spatial resolution, intensity, bit-depth etc.
0
255

## Slide 10: Image formation process
An image is a representation of a real object.
But the representation is imperfect:
  Blur and noise degrade the image.
  Digitization discretizes the intensity information.
  …
real object
digital image
image acquisition
Notes: Light source > Light > Lenses > Object > Camera > Read out camera (discrete px and values)
Other degradation: flatfield (inhomogeneous illumination) and darkfield (camera offset)

## Slide 11: Image formation is not perfect.
General image degradation by blur and noise.
Inhomogeneous illumination (flatfield) and signal offset (darkfield)
Discretization of information
theoretical image
observed image
Blur is inherent to microscope optics.
PSF
PSF: https://en.wikipedia.org/wiki/Point_spread_function
flatfield
darkfield
*
+
=
observed image
Notes: Darkfield: = signal that is measured at camera even though the shutter is closed (in particular widefield. For LSM we can adjust the offset)

## Slide 12: Image dimensions
Images have up to 5 dimensions.
2D 3D (z-stack)
+ time + channels
A dataset can additionally consist of multiple tiles or views.

## Slide 13: Image metadata
Metadata provides crucial additional information on the image.
Very import meta info: spatial scale.
Notes: An image without meta info (how acquired, scale, …) is worth little.

## Slide 14: Pixel size (sampling)
Pixel size is the actual physical size of a pixel in an image.
On camera-based microscopes it is controlled by the magnification.
Width of 1 pixel = 0.05 um
Therefore: 1/0.05 = 20 pixels/ um

## Slide 15: Optical resolution
Optical resolution is a property of the imaging system and determined by the type of microscope and objective.
It is defined as the minimum distance between two point objects to still be separable (see: PSF, Airy disc).
The optical resolution in axial direction (z) is lower than in lateral direction (x,y).
PSF confocal: SVI Huygens Nyquist calculator: https://svi.nl/NyquistCalculator
Point objects: http://physwiki.apps01.yorku.ca/index.php?title=File:Fig15_airy.png
PSF from confocal microscope
Notes: Usually undersampling in z is the bigger issue. But if sampled high enough: consider deconvolution for resolution improvement

## Slide 16: Nyquist–Shannon sampling theorem
Sampling frequency must be 2-3x larger than the smallest object you want to detect.
  That means: at least(!) 3 pixel per and between objects (better more!).
  Further reading: https://en.wikipedia.org/wiki/Nyquist-Shannon_sampling_theorem
To make use of the full optical resolution: Sample at 3x the optical resolution.
  Nyquist calculator: https://svi.nl/NyquistCalculator
Image sources:
Elena Gromberg, Tanaka Group, CRTD Dresden
Cromey: Avoiding Twisted Pixels,

## Slide 17: Quiz
The length of the red line drawn on the image is 95 pixels.
Based on the scale bar, what is the image’s pixel width?
0.5 µm
0.01 µm
0.05 µm

## Slide 18: Bit-depth
The bit-depth n enumerates how many different intensity values are present in an image:
  2n grey values
In microscopy, images are usually stored as 8, 12 or 16-bit images.
1
2
3
4
5
6
7
8
1
2
16
Slide courtesy: Robert Haase

## Slide 19: Lookup tables (LUTs)
The lookup table decides how the image is displayed on screen.
Applying a different lookup table doesn’t change the image. All pixel values stay the same, they just appear differently
Pixel value
Display color
0
1
2
…
255
Pixel value
Display color
0
1
2
…
255
Pixel value
Display color
0
1
2
…
255
Slide courtesy: Robert Haase

## Slide 20: Lookup tables (LUTs)
Choose visualization of your color tables wisely!
Think of people with red/green blindness!
Default view
Red/green blind people see it like this
Replace red with magenta!
Slide courtesy: Robert Haase

## Slide 21: Quiz
Which intensity does the marked pixel have?
0
64
256
192
128
0
64
128
0
64
256
192
128
192
Slide courtesy: Robert Haase

## Slide 22: Image Histogram
All pixels of an image are counted and binned according to their value.
A histogram is a 1D summary of an image.
Number of pixels
Intensity
Background?
Object?

## Slide 23: Image Histogram

## Slide 24: Multichannel images
In microscopy, channels are usually acquired separately with a monochrome camera.
For a composite view, the channels are colored with different LUTs.
  Coloring according to wavelength or for optimizing good contrast.

## Slide 25: Color Images (RGB)
Color images are usually composed of RGB channels with 8bits per channel.
They are acquired with a color camera (e.g. photography).
Tip: Applications like MS Office cannot display multichannel images. Convert the image to RGB for export. This is non-reversible – work on an image copy!
Red Green Blue decomposition
RGB Image
Notes: Alternative color decomposition: Alternative: HSV decomposition

## Slide 26: Color spaces
Color images are often RGB – color is described by the 3 channels: red, green, blue.
Another common decomposition: CMYK
CIE commission established other color spaces which are closer to how colors are perceived by humans.
  Most notably: CIELAB color space: L*a*b*
  L (lightness), a (green/red), b (blue/yellow)
  Perceptually uniform: Changes in L*a*b* values corresponds well to changes in human color perception (this is different for RGB).
Tip: Explore different color spaces.
  Objects which are hard to distinguish with an algorithm in RGB space may be easier to distinguish in CIELAB space.
Image sources:
cube: wikipedia
CIELAB: XRite
Notes: Monochrome camera (microscope) versus color camera -> color spaces matter for the latter
Color space conversion: think of it like a coordinate transform (but actually this is not quite true: non-absolute color space)
CIE: international commission on Illumination
RGB: corresponds to physical color difference – but two physically different colors may look quite uniform to a human

## Slide 27: File formats
Common file formats for image saving.
tiff / tif
  Very versatile (multichannel, zstacks, various bit depth, etc.).
  Good with meta data.
  Large file size
  Use as default
hdf5 / h5
  Specially developed for viewing and processing large data
png
  Compressed but not lossy: small file sizes
  Less powerful than tiff (metadata etc.)
  Convenient for image export for presentations.
jpg / jpeg
  Lossy compression.
  Do not use this!
jpg artifacts

## Slide 28
Tools for image analysis

## Slide 29: Image Analysis Software
Free/Commercial,
Customizable versus ease of use
Specific pipelines: slide analysis, HCS, neurons, 3D visualization,
large dataset
CellProfiler
MATLAB
ImageJ/Fiji
Imaris
Ilastik
Python
Huygens
Notes: Describe categories of software available

## Slide 30
Introduction to FIJI Image characteristics and visualization

## Slide 31: Image Analysis Software: FIJI
Swiss army knife of biological images
Multiplatform
Good user/developer base
Versatile data reader
Wide range of plugins supported
Multiple level of interactions
  Many tools
  Macro/scripting
  High level image analysis API

## Slide 32: FIJI: Menu and Interface
Menu
Tool bar
Status bar

## Slide 33: Command Finder
Press the “L” key and start typing in the search bar.
It is a very powerful tool – and helps navigating through confusing menus.
Notes: Any color can be chosen for the channel
Functional meaning of the protein

## Slide 34: Opening images with FIJI
Methods:
  Drag and drop
  File > Open > …
  File > Import > …
Bio-formats support
  Can open proprietary
  file formats (.czi, .lsm, …)
Image sequence
Tip:
You can also drag Results tables, Scripts etc to Fiji to open them.

## Slide 35: Image Interface
Zoom factor
(use +/- keys)
Image bit-depth
Image size in physical units (and in pixels)
Dataset positions
c = channel
z = slice
t = time frame

## Slide 36: Image Navigation
Press “space” and left click on the image to pan it
Press “+” or “-” to zoom in and out.
Point the region to zoom in with the mouse

## Slide 37: Image meta-data
Image > Show Info…
Image > Properties…

## Slide 38: Spatial scale bar
A scale bar is important when presenting images.
“Is an object in the image 50um or 1000um?”: Hard to tell without scale bar.
Analyze > Tools > Scale Bar …

## Slide 39: Viewing pixel values
Value at current mouse position
Values along a line selection Analyze > Plot Profile …

## Slide 40: Image histogram
Analyze > Histogram
Notes: Just for reference for this image: AuPb was blurred previously with gaussian, sigma=1

## Slide 41: Brightness & Contrast
Adjusting brightness & contrast changes the display range (windowing) of the image.
Image > Adjust > Brightness/Contrast… or Cmd/Ctrl+Shift+C
0
255
85

## Slide 42: Brightness & Contrast
Adjusting the display range does not change the pixel values - it is just a visualization.
Careful: “Apply” changes the pixel values and remaps them to the current display range – this is irreversible!
  Don’t use this. Unless you need it for visualization – then use with care.
saturation
Notes: Can you on histogram: saturated + zero pixels + gaps in intensity

## Slide 43: Multichannel images
Composite image: visualize image with multiple channels simultaneously
In FIJI, Image> Color> Make Composite, Image> Color> Channels tool.. for more
Image> Color > Split channels

## Slide 44: RGB vs composite images
Convert RGB to Composite: Image > Color > Make Composite

## Slide 45: Lookup tables
Image > Lookup Tables
HiLo
(shows saturation)

## Slide 46: Color calibration Bar
Analyze > Tools > Calibration Bar…
Recommended when using non-standard LUT (Fire, Spectrum..)
Adds a ramp to show which color represents which gray-value.

## Slide 47: Setting Fiji up properly
Common issues to better fix right away:
Images should have white objects on black background:
  Go to Fiji> Process> Binary> Options
  Set Black background = True
Allocate maximum memory to be used by FIJI
  Go to Fiji> Edit > Options > Memory and Threads
  Do not use command launcher for setting this

## Slide 48: Fiji Update Sites
The Fiji Updater updater lets you subscribe to many plugins and extends your toolbox.
It checks automatically for updates and helps keeping Fiji up-to-date.
Fiji: Help > Update ….
“Apply changes” to update, then restart Fiji.
Update Fiji frequently.
  If you worry about reproducibility: First create a copy of Fiji and store it together with the analysis.

## Slide 49: Adding an update site
Run the updater explicitly by going to Help> Update…
Select Manage Update Sites to bring up a window of all the updates sites.
Select the ones you want and click on Close to add these updates.
Choosing Add update site allows you to add a website manually.
Click “Apply changes” to update, then restart Fiji.
See also: https://imagej.net/Following_an_update_site
Notes: Do we also need to show advanced mode?

## Slide 50: Image.sc Forum: Getting Help
https://forum.image.sc/
Very active forum on image analysis
  For all user levels
  For conceptual questions, technical issues, announcements etc.
  Often you get help very quickly.
Tips:
  Be nice – the people who help you are volunteering.
  If you know an answer: help others.

## Slide 51: Demo
Image properties, pixel values, LUTs, command finder, bit depth, channel control, brightness & contrast, …
Used data for demo:
AuPbSn40.tif
hela-cells.tif
Clown.jpg

## Slide 52: Quiz
In Fiji, open the Fly Brain image (File > Open Samples > Fly Brain (1MB)) and display its metadata window and properties window.
What is the height of this image in microns?
What is the pixel width?
256
684.93
2.67 um
3.94 um

## Slide 53: Bit depth: Converting the image type
Examples:
  16-bit -> 8-bit: Irreversible!
  8 bit -> 16 bit: No problem. Higher bit-depth is always ok.
  Multichannel composite -> RGB: usually irreversible!
Image type conversion can be irreversible. Information is then lost and cannot be recovered.
Never do lossy conversion for quantitative analysis. Only use for visualization (of a copy of) the image.

## Slide 54: Bit-depth Conversion: 16bit -> 8bit
Scenario:
  Images were acquired at 16bit to maximize the recorded information.
  But for a presentation in PowerPoint you need an 8bit version of it – otherwise it would look black.
Why is this not trivial?
  16bit: possible values: [0, 65535]
  8bit: possible values: [0,255]
Different options for mapping the two ranges:
65535
0
0
255
65535
0
0
255
65535
0
0
255
no scaling
scale full range
custom scaling (adjusted to image properties)

## Slide 55: Bit-depth Conversion: 16bit -> 8bit
In Fiji: Image > Type > 8-bit
“Scale when converting” in Edit > Options > Conversions should usually be checked.
But Caution! The min-max values for scaling are taken automatically from the min–max in the Brightness & Contrast window.
For converting multiple images of an experiment: Always set min-max to the same value before conversion.

## Slide 56: Exercise
Prepare image for presentation
  Open the image cell_layer2.tif
  Split channels
  Merge channel 1 and 3
  Update channel 1 LUT to magenta
  Adapt contrast of each channel
  Convert type to RGB
  Add a scale bar
  Save as Tiff
  Try to load in a ppt/keynote
Notes: Scale bar should not be visible : Flatten again = convert to RGB

## Slide 57: Exercise
Bit-depth conversion
Open zfish_retina.tif
Extract first channel, set LUT to gray.
What is the bit depth?
Measure a profile along a line.
For every conversion work on a separate duplicate.
Always measure the profile after conversion.
(A) Convert to 8 bit (Image > Type > 8-bit).
(B) First change the Brightness & Contrast display. Then convert to 8-bit.
(C) Uncheck scaling temporarily. Then convert to 8-bit.
  Edit > Options > Conversions
  Turn scaling on again.

## Slide 58: Summary
d
Image
Pixel value, Bit depth
Grey level image
Histogram
Pixel Size
Visualisation
B&C
LUTs
RGB, Composite Images
Channels tool

## Slide 59
ROI & Measurements

## Slide 60: ROI: Region of Interest
Region tools:
  Rectangle, rounded rectangle
  Oval, orientable ellipse, brush tool
  Polygon, free form, Wand tool
Line tools:
  Straight, segmented, free
Point tools:
  Point, Multi-Point
Interactively edit ROIs
Double click to see the options

## Slide 61: ROI: Region of Interest
There are more tools in the toolbar than visible
Use right-click and double-click to uncover them

## Slide 62: ROI: Region of Interest
draw a rectangle
using the rectangle tool
draw a circle
using the circle tool
add objects to the ROI
by holding SHIFT
unite objects to the ROI
by holding SHIFT
subtract objects to the
ROI by holding ALT
move the ROI
by clicking inside and move the mouse
delete the ROI
by clicking outside
Recover the last ROI
by using menu Edit > Selection > Restore Selection (SHIFT+CMD+E)

## Slide 63: ROI Measure Workflow
Open an image
Select a tool and draw ROI
Analyze > Set measurements
Analyze > Measure
Creates results table
Select Table
File > SaveAs
Export data for analysis

## Slide 64: The ROI Manager
In Fiji, Analyze> Tools > ROI Manager…
Helps in storing and dealing with multiple ROIs
Press key “T”

## Slide 65: The ROI Manager
Visualize, label and measure ROIs

## Slide 66: The ROI Manager
Additional functions available:
Combine multiple ROIs (OR)
Split ROIs (Split)
Save
…

## Slide 67: Quiz 4
  You can rename a ROI
  You cannot change the ROI outline color
  You can save a ROI as a file
True
False
True
False
True
False
Open the ROI manager Analyze> Tools > ROI Manager… and check the functions.
Now answer TRUE or FALSE to the statements about ROI Manager

## Slide 68: Image Overlay
Non-destructive visualization of outlines.
Adds ROIs to an extra image layer which is for display only and can be toggled on/off.
In FIJI, draw a ROI, then: Image> Overlay>Add Selection.
Image from: http://blogs.qub.ac.uk/ccbg/files/2014/05/2014-05_Analyzing_fluorescence_microscopy_images.pdf
To create an image for PowerPoint: Burn the overlay into the image:
  Image > Overlay > Flatten
  Careful! This changes the images and the outline cannot be removed again!
Notes: The “show all” in ROI manager creates implicitely an Overlay.

## Slide 69
Demo
ROIs, ROI manager, measure, set measurements, overlay, …
Used data for demo:
FluroescentCells.tif

## Slide 70: Exercise
Measure embryo average size
  Open embryos.tif
  Use Line ROI to measure diameter of e.g. 5 embryos
  Save the result table, then clear it.
  Draw the outline of an embryo to the ROI manager. Repeat for a few embryos.
  Measure area and intensity.
  Add an overlay to the image and save it
    Either ROI by ROI (“add Selection”)
    Or “Roi Manager > Show All” (Creates an overlay).
  Flatten image and save it too
  Open image in IJ and PPT

## Slide 71: Summary
ROI manager
Overlay
Measure pipeline

## Slide 72
Counting Objects

## Slide 73: Finding Objects
Object detection
Point/Box per object
Use cases:
Counting
Tracking spots
Object segmentation
Outline per object
Uses cases:
Shape quantification
Spatial relation of objects
Notes: Detection is easier
Spatial relation between objects: e.g. neighbors, what is inside/outside of cells

## Slide 74: Object detection
There are multiple ways for detecting objects. Examples:
Template matching: https://scikit-image.org/docs/dev/auto_examples/features_detection/plot_template.html
Intensity maxima
Spots/Blobs
Template matching
Notes: Maxima: single brightest point
Spots/Blobs: searches for spots of specified size

## Slide 75: Image maxima: counting objects
An image can be imagined as a landscape of hills and valleys
Counting objects: detect how many peaks or hills are there in the image!

## Slide 76: Counting objects in Fiji
In FIJI, use Process > Find Maxima.. to detect peaks in an image
Easy way to do a quick counting of objects
Pipeline: Open image, find maxima, measure

## Slide 77: Find maxima menu
How high is the peak value from its base (~dynamic range)
Include/exclude maxima at the edge of the image
Preview the detected points
Are objects on light or dark bg
Various output options
Photo: http://fwp.mt.gov/mtoutdoors/HTML/articles/2013/peakbagging.htm#.V-P1NvArIdU
More info (on “strict” option): https://forum.image.sc/t/new-maxima-finder-menu-in-fiji/25504/9

## Slide 78: Find maxima menu
Possible outputs from maxima finder

## Slide 79
DEMO
Used data:
Spot_detection.tiff

## Slide 80: Other tools: ComDet
Fiji plugin for finding “roundish” objects in image of specified size
  Spots, vesicles, droplets, dots, etc.
Plugins > ComDet Detect Particles
https://github.com/ekatrukha/ComDet/wiki/How-to-use-plugin-%28Text-Tutorial%29
Features:
Preview function
Option to detect in a ROI
Option to do colocalization (shows up when you open 2-ch image)
Results table

## Slide 81: Exercise
Count spots
Open nuclei_transcripts_zebrafish.tif
Split channels and work on channel 1. Crop it.
Use Maxima Finder menu to count number of spots in the image
List their coordinates
Vary the prominence, strict and exclude the edge parameters and identify the changes in maxima detection

## Slide 82: Summary
Counting: Maxima detection
Detection vs Segmentation
FIJI Find Maxima