## Slide 1: Introduction to Image Analysis with FIJI
Noreen Walker, Gayathri Nadar
Scientific Computing Facility, MPI-CBG
3.-7.5.2021
2. Segmentation &
Filters, Morphological Operations
Aim of this session:
Segmentation introduction
Classic segmentation pipeline, interactive segmentation
Provide mathematical background for operations on images:
  Image filters, Morphological operations, Image math
With material from:
Robert Haase
Benoit Lombardot

## Slide 2: Course schedule
Day 1 (Mon 3.5.)
  Image basics, visualization, measurements
  Spot detection
  Segmentation (start)
Day 2 (Tue 4.5.)
  Visit LMF
  Segmentation (cont’d)
  Mathematical background: image filters, morphology
Day 3 (Wed 5.5.)
  Advanced segmentation: Machine learning with Ilastik
  IJ Macro (start)
Day 4 (Thu 6.5.)
  IJ Macro (cont’d)
  3D data: visualization and analysis
Day 5 (Fri 7.5.)
  Image registration, image stitching
  Time sequence analysis and tracking
  Good practices

## Slide 3: Recap: Basic Concepts
d
Image
Pixel value, Bit depth
Grey level image
Histogram
Pixel Size
Visualisation
B&C
LUTs
RGB, Composite Images
Channels tool

## Slide 4: Recap: Basic Concepts
ROI manager
Overlay
Measure pipeline

## Slide 5: Recap: Counting objects
Counting: Maxima detection
Detection vs Segmentation
FIJI Find Maxima

## Slide 6: Quiz (1/2)
This histogram shows the grey value distribution of which image?

## Slide 7: Quiz (2/2)
You have an image with an overlay in red and a Roi selection in yellow.
When you press the key M (measure), which region will be measured?
Overlay
Full image
Roi

## Slide 8
Segmentation

## Slide 9: Overview
Segmentation introduction
Classic segmentation pipeline
  Preprocessing, thresholding, postprocessing
  Particle analysis and measurements
Application: Interactive segmentation

## Slide 10: Finding Objects
Object detection
Point/Box per object
Use cases:
Counting
Tracking spots
Object segmentation
Outline per object
Uses cases:
Shape quantification
Spatial relation of objects
Notes: Detection is easier
Spatial relation between objects: e.g. neighbors, what is inside/outside of cells

## Slide 11: Goal
Determine the cell regions (objects) automatically and measure their properties.
Image Source: Jaydeep Sidhaye, Norden Group, MPI CBG

## Slide 12: How to split an image into regions?
Many methods for segmentation exist.
Image by: Ignacio Arganda-Carreras, Biological Image Reconstruction and Analysis Course, 2016

## Slide 13: How to split an image into regions?
Thresholding
Machine learning: supervised pixel classification
Unsupervised learning: Clustering
Region growing: from seed points
Examples
Image: https://morioh.com/p/dcdc9957bc1c
Notes: Thresholding: simple but often works
Pixel classification: also quite simple to do.
Start with red in course, then gray.

## Slide 14
Classic segmentation pipeline

## Slide 15: Typical pipeline
Preprocessing
Deconvolution
Denoising/ Smoothing
Data reduction
Background correction
….
Segmentation
Thresholding
Pixel classifiers (machine learning)
Region growing
Edge based segmentation
…
Postprocessing
Morphological operations:
Watershed
Fill holes
Opening/Closing,…
…
Preprocessing
Segmentation
Postprocessing
Analysis
Analysis
Counting
Measure properties
…

## Slide 16: Preprocessing: Denoising
Reduce the effects of noise using Gaussian Blur
Oh no! I see thousands of white objects!
Thresholding
Ok, it’s just 4 objects.
Thresholding
Blurring
In Fiji:
Process > Filters > Gaussian blur
Or:
Process > Smooth

## Slide 17: Preprocessing: Subtract Background
If the background is uneven, objects can be hard to segment.

## Slide 18: Preprocessing: Subtract Background
If the background is uneven, objects can be hard to segment.
Remove flatfield in the background.

## Slide 19: Preprocessing: Subtract Background
If the background is uneven, objects can be hard to segment.
Remove flatfield in the background.

## Slide 20: Subtract Background in Fiji
> radius of largest object to be detected
In Fiji:
Process > Subtract Background …

## Slide 21: Thresholding
Thresholding is used to create a mask of foreground objects in an image.
It is the simplest form of segmentation.
In FIJI menu, Image > Adjust > Threshold or Cmd + shift + T
Always use an automatic method for threshold selection
-> reproducibility.
Switching dark background inverts the selection.
Apply creates a mask.

## Slide 22: Demo/Hands-on
Goal: Importance of preprocessing before thresholding
Remember: Garbage in, garbage out!
Activity: Threshold image with and without background subtraction

## Slide 23: Thresholding Methods
Automatic thresholding methods compute the threshold based on the image histogram.
Otsu method:
  Maximize the variance between the two classes of pixels, which are separated by the threshold.
  Equivalent: Minimize the variance with each class.
  -> Works well for bimodal distributions.
https://scikit-image.org/docs/0.10.x/auto_examples/plot_otsu.html

## Slide 24: Choosing the thresholding method
It is easy to compare all automatic thresholding methods in Fiji.
In FIJI, Image > Adjust > Auto threshold with try all checked.
Before picking your method, test it on a few of your images.
Montage
of outputs
Side note: Local thresholding:
This is a method where the threshold value is not global but changes locally.
The threshold at each pixel is computed based on the intensity in its local surrounding.
Image > Adjust > Auto local threshold: Compare methods.

## Slide 25: Quiz
A
B
We have applied two thresholding methods on the image on right and the results are below.
Which method/solution do you think is better?
Input
Notes: Answer: it depends on what is biologically relevant – for intensity measurements: best to have an independent channel for segmentation. Otherwise the segmentation depends on the threshold value
In this case: probably the right box -> detect all nuclei

## Slide 26: Postprocessing: Mask cleanup
Process > Binary > Fill holes
Process > Binary > Watershed (split objects)
Process > Binary > Open [then] Close (remove small objects)

## Slide 27: Postprocessing: Binary Watershed
Watershed
Split touching objects.
Model: Objects are roundish and touch at a “thin neck”.

## Slide 28: Binary Watershed
Binary segmentation
Distance map
Slide courtesy: Robert Haase
The watershed algorithm for binary images allows cutting one object into two where it’s reasonable.

## Slide 29: Binary Watershed
The watershed algorithm for binary images allows cutting one object into two where it’s reasonable.
The watersheds are made from binary images. The algorithm does not take the original image into account!
Binary segmentation
Distance map
Original image
Watershed
Slide courtesy: Robert Haase

## Slide 30: How many regions do we have?
Different algorithms expect different input.
Mask or Binary image or Thresholded image
Foreground (255) vs Background (0)
Label image
Each region has a unique value (background=0, cell1=1, cell2=2, etc.)
Connected component labelling
1 region!
14 regions
Naming conventions

## Slide 31: Measuring region properties
A segmented object can be described by many properties.
Geometric properties
Area
Centroid
Bounding box
Perimeter
Ellipsoid fit
Major & minor axis
…

## Slide 32: Measuring region properties
A segmented object can be described by many properties.
Intensity properties (from original image)
  Mean
  Standard deviation
  Median
  …

## Slide 33: Fiji: Set Measurements
Set the measurements before doing particle analysis.
In FIJI, Analyze -> Set Measurements
Includes option to redirect a measurement
Analyze these particles…
…but take measurements (intensity etc) from this image.

## Slide 34: Fiji: Particle Analyzer
Fiji: Analyze > Analyze Particles …
?

## Slide 35: Optimizing the Segmentation Pipeline
Pre-processing
Segmentation / Regionalisation
Post-processing / correction
Measurement
Results not good?
Change analysis parameters
Change imaging settings
Notes: Recap of the pipeline

## Slide 36: Add-on: ROI versus Mask (Fiji)
ROIs and Masks in Fiji can be converted into each other.
Edit > Selection > Create Selection
Edit > Selection > Restore Selection
Edit > Selection > Create Mask

## Slide 37: Add-on: MorphoLibJ (Fiji)
A great library for segmentation and post-processing.
Well documented! (https://imagej.net/MorphoLibJ)
Subscribe to the update site: Help->Update…->Manage Update Sites: add IJPB-plugins
Some useful tools for post-processing:
Remove small regions
Keep largest region

## Slide 38: Demo: Segmentation
Data obtained from Elnaz Fazeli, Univserity of Turku

## Slide 39: Exercise: Segmentation
Segment cells, measure each cell brightness, and get cell count. (Cell_2D_bg.tif)
Preprocess with gaussian blur
Subtract background
Duplicate this image to re-use for measurements.
Threshold
Optional: Open/Close, Watershed
Set measurements (Don’t forget to redirect)
Analyze particles
Tips:
Use the search bar (key L) if you don’t find a command.
Duplicate your image regularly as backup (Cmd+Shift+D) 
Use the ‘Preview’ buttons
More datasets to segment:
cell_chain.png, cell_colony.tif (use Binary > Open or MorpholibJ to remove small regions)

## Slide 40
Application:
Interactive segmentation

## Slide 41: Interactive segmentation
Interactive segmentation can be used for:
Find good parameters before automatizing the pipeline (exploration).
Quick segmentation of a single image (exploration).
Segment difficult data.

## Slide 42: Concept: Grayscale Watershed
Recap: Binary watershed
Grayscale watershed
  The peaks (or minima) are directly detected in the grayscale input image.
  The input is therefore a grayscale image, not a binary image.
Start flooding
Compute distance map.
Find local peaks
Stop flooding once regions touch or an intensity threshold is reached
Binary image
Notes: Binary vs grayscale: in binary the distance map is implicitly calculated, to find local maxima

## Slide 43: Segmentation with Interactive H_Watershed
(Interactive) H_Watershed plugin from SCF
  Works directly on the grayscale images
  Allows for interactive exploration.
  In FIJI, SCF > Labeling > (Interactive) H_Watershed
Note:
  Need SCF MPI CBG update site.
  Preprocessing same as before.
Sample image for which our simple pipeline could fail
https://imagej.net/Interactive_Watershed

## Slide 44: Interactive H_Watershed
Seed dynamics:
Prominence of a maxima as compared to its surrounding.
Only maxima with high prominence are used as starting points for regions.
Low value
High value
Careful: LUT is inverted in these images. This plugin locates the maxima (not minima).
SCF > Labeling > (Interactive) H_Watershed

## Slide 45: Interactive H_Watershed
Intensity Threshold:
Limits the total amount of flooding.
Pixels with values below a threshold (i.e. darker) will not be filled.
Low value
High value

## Slide 46: Interactive H_Watershed
Image
Contour
Overlay
Solid
Overlay

## Slide 47: Interactive H_Watershed
Box unchecked
Box checked
MorpholibJ Region Analyzer
Plugins › MorphoLibJ › Analyze › Analyze Regions
Standard Particle Analyzer
Analyze > Analyze Particles

## Slide 48: Interactive Marker-Controlled Watershed
Interactive Marker-Controlled Watershed (MorpholibJ)
User places seed-points manually (at intensity minima!)
Grayscale watershed: Image is flooded from the seed points
In FIJI, Plugins › MorphoLibJ › Segmentation › Interactive Marker-controlled Watershed
Note:
  Need IJPB-plugins update site.
  Preprocessing same as before.
https://imagej.net/Interactive_Marker-controlled_Watershed

## Slide 49: Exercise: Interactive Segmentation
Segment the cells in cells Drosophila_2D_Race_inverted.tif .
Duplicate the image
Do you need some preprocessing?
Use Interactive H_Watershed: SCF > Labeling > (Interactive) H_Watershed
Analyze the segmented image.
Measure for each cell its average intensity (from the input image):
Use either Particle Analyzer: Analyze > Analyze Particles …
Or Region Analyzer: Plugins › MorphoLibJ › Analyze › Analyze Regions
Make sure you have the right input image for the analyzer tool.

## Slide 50: Summary
Watershed: split regions
Preprocessing
Segmentation
Postprocessing
Analysis
Classic segmentation pipeline
Region segmentation
Binary image
Labels

## Slide 51
Concepts:
Filters, Morphological operations

## Slide 52: Overview
Mathematical background for operations on images
Image filters
  Linear filters (convolutions)
  Nonlinear filters
Morphological operations
Image math
  Calculations with images

## Slide 53
Image Filters

## Slide 54: Spatial filters
An image processing filter is an operation on an image.
Filters change pixel values.
Filters do not do magic. They can not make things visible which are not in the image.
Application examples
  Noise-reduction
  Artefact-removal
  Contrast enhancement
  Correct uneven illumination
We already used several filters in the previous segmentation pipeline.
Image source: Mauricio Rocha Martins (Norden/Myers lab, MPI CBG)

## Slide 55: Example: Noise removal with filters
Original image
Gaussian blur filtered
Median filtered
Linear filter
Nonlinear filter
Image source: Mauricio Rocha Martins (Norden/Myers lab, MPI CBG)

## Slide 56: Linear Filters
Linear filters replace each pixel value with a linear combination of surrounding pixels
  Basically, linear filtering is a Convolution
  It needs a kernel (weight template)
Result: new image where each pixel is replaced by the weighted sum of pixel values in the neighbourhood.
Kernels are matrices describing a linear filter.
1/9 | 1/9 | 1/9
1/9 | 1/9 | 1/9
1/9 | 1/9 | 1/9
Mean filter, 3x3 kernel
Animation source: Dominic Waithe, Oxford University
https://github.com/dwaithe/generalMacros/tree/master/convolution_ani
1/16 | 1/8 | 1/16
1/8 | 1/4 | 1/8
1/16 | 1/8 | 1/16
Gaussian filter, 3x3 kernel

## Slide 57: Linear Filters
Terminology:
  “We convolve an image with a kernel.”
  Convolution operator: *
Examples
  Mean
  Gaussian blur
  Sobel-operator
    X/Y-Gradient
-1 | 0 | 1
-2 | 0 | 2
-1 | 0 | 1
*
1 | 1 | 1
1 | 8 | 1
1 | 1 | 1
*
=
=
    Total gradient:

## Slide 58: Linear Filters in Fiji
Linear filters:
Gaussian blur
Mean
  * Smooth is a 3x3 Mean filter
Convolve…
  Allows us to specify our kernel
*

## Slide 59: Nonlinear Filters
Non linear filters also replace pixel value inside a rolling window but in a non linear function.
Examples: order statistics filters
  Min
  Median
  Max
  Variance
  Standard deviation
75 | 85 | 60
67 | 73 | 91
50 | 88 | 59
[ 50 59 60 67 73 75 85 88 91 ]
Min
Median
Max

## Slide 60: Nonlinear Filters in Fiji
Examples:
  Min
  Median
  Max
  Variance

## Slide 61: Edge detection filter
Edge detection might make sense to measure surfaces or follow structures which are located between bright and dark structures.
Median filter+ Edge detection
nuclear envelope marked with Lap2b-GFP
+ median filter
Microscopists may know fancy alternatives to computational edge detection.
Image source: Mauricio Rocha Martins (Norden/Myers lab, MPI CBG)
Fiji: Process > Find Edges …

## Slide 62
Morphological operations

## Slide 63: Morphological operations
Morphological operations are image filters which are used on binary masks.
Goal: Improve the binary mask.
Some of the morphological operations:
  Dilation
  Erosion
  Opening
  Closing
  Watershed
  Fill holes
We already used several morphological operations in the previous segmentation pipeline.
Slide adapted from: Elnaz Fazeli, University of Turku

## Slide 64: Dilation
Dilation: Grows regions.
If any pixel in the neighborhood is white, then the central pixel is converted to white.
Gray value equivalent: Maximum
https://www.edx.org/course/image-processing-and-analysis-for-life-scientists
Slide courtesy: Elnaz Fazeli, University of Turku
8-connected
neighborhood
4-connected
neighborhood
Dilation
Notes: Colors just for illustration: we only have black and white pixels

## Slide 65: Erosion
Erosion: Shrinks regions.
If any pixel in the neighborhood is black, then the central pixel is converted to black.
Gray value equivalent: Minimum
Slide courtesy: Elnaz Fazeli, University of Turku
Erosion

## Slide 66: Refining masks: Erosion & Dilation
Erosion and dilation combined allow correcting outlines.
Erosion
Dilation
“Opening”

## Slide 67: Refining masks: Erosion & Dilation
Morphological filters can be combined in many ways:
Erosion: Set all pixels to black which have at least one black neighbor.
Erosion
Erosion
Erosion
Dilation
Erosion
Closing: Dilation + Erosion
Dilation
Dilation
Dilation
Dilation: Set all pixels to white which have at least one white neighbor.
Opening: Erosion + Dilation

## Slide 68: Quiz (1/2): Morphological Operations
Assuming white pixels have value 1 and black pixels have value 0.
With which filter is the Erosion filter in this context identical?
Tip: Check what the influence of the neighborhood (green) on a single pixel (red) is when updating it.
0
0
0
0
0
0
1
1
1
0
0
1
1
1
0
0
1
1
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
Erosion
Mean
Minimum
Maximum

## Slide 69: Quiz (2/2): Opening / Closing
How is the combination of dilation + erosion called again?
Dilation
Erosion
Opening
Closing

## Slide 70: More morphological operations
Distance Map
Binary Watershed
Skeletonize
Fill holes
….
Binary segmentation
Distance map
Watershed

## Slide 71: Morphology in Fiji
Mask
+ filled holes
+ Watershed

## Slide 72
Image math

## Slide 73: Background removal
Differentiating objects is easier if their background intensity is equal.
Depending on the effect we want to correct for, it might make sense to divide an image by its background instead of subtracting it.
Original image
Extracted background
Subtracted background
Image divided by background
Image source:
Mauricio Rocha Martins (Norden/Myers lab, MPI CBG)
This is roughly what the Fiji “Subtract Background…” is doing.
Original image
Extracted background
-
=
/
=
Notes: This is a mathematical

## Slide 74: Mathematical operations on images
It might be hard to differentiate objects from single images…
Segmentation of nuclei can be improved by subtracting a channel visualizing nuclei envelope from the nuclei channel.
-
=
Image source: Mauricio Rocha Martins (Norden/Myers lab, MPI CBG)

## Slide 75: Mathematical operations on masks
Or
And
Notes: Can write logical operations if necessary on the screen

## Slide 76: Image math in Fiji
Fiji: Process > Image Calculator
Use the Image Calculator to subtract, add, multiply or divide images.
Image source: Mauricio Rocha Martins (Norden/Myers lab, MPI CBG)

## Slide 77: Math with numbers + images in Fiji
All basic math operations for pixels are available in ImageJ/Fiji.
If you want to simulate a binary image: Select some black pixels and add 255 to make them white.

## Slide 78: Demo
Morphology
  Use image: nuclei_transcripts_zebrafish_zoom_1ch.tif
  Thresholding
  Erosion, Dilation
Distance Map
  Use image: mask1.tif
  Distance transform for original and inverted image
Image calculator: Combining masks
  Use images: mask1.tif, mask2.tif
  AND, OR

## Slide 79: Exercise: Filters
*
Open the example zfish_retina.tif in Fiji.
Image > Colour > Split channels
Play with linear and non-linear filters in the menu Process > Filters.
Change the radius parameter. Enter 1, 2, 5, and 50!
Compare Smooth and Gaussian Blur… what’s different?
Original image
Gaussian blur filtered
Median filtered
Image source: Mauricio Rocha Martins (Norden/Myers lab, MPI CBG)

## Slide 80: Exercise: Distance Map
Compute the distance of the spots to the nucleus.
Open nuclei_transcripts_zebrafish_zoom.tif.
Split channels.
Segment the nucleus.
Detect the spots.
Measure their distance to the nucleus region.
Tips: Thresholding, Maxima detection, Distance map/transform
Notes: EXTRA

## Slide 81: Exercise: Image calculator
Process the image “zfish_retina.tif” using
  Background subtraction
  Image Calculator
Goal: Optimize differentiation between cells.
Then create a segmentation mask.
Image source: Mauricio Rocha Martins (Norden/Myers lab, MPI CBG)
Background subtraction (radius = 25)
Subtraction

## Slide 82: Optional Exercise: Making your own filters
Open zfish_retina.tif
Split the channels.
Make your own filter kernels!
Use the menu Process > Filters > Convolve…
1 | 1 | 1
1 | 8 | 1
1 | 1 | 1
-1 | -1 | -1
-1 | 8 | -1
-1 | -1 | -1
1 | -2 | 1
1 | -2 | 1
1 | -2 | 1
1 | 1 | 1
-2 | -2 | -2
1 | 1 | 1
Image source: Mauricio Rocha Martins (Norden/Myers lab, MPI CBG)

## Slide 83: Summary
Image Filters
Image Math
Morphological Operations

## Slide 84: Segmentation methods
Segmentation with thresholding is a simple pipeline and often works.
Recall that also many segmentation other methods exist.
Examples:
Pixel classification with (shallow) Machine Learning
  -> powerful
  -> next session
Deep Learning (Neural nets)
  Examples: StarDist, CellPose
  -> very powerful
Notes: From simple to more complex methods
But the 2 nnet examples are very usable

## Slide 85: Advanced segmentation: StarDist
“StarDist”
  a neural net for segmenting roundish, dense objects (like nuclei)
Pretrained net available as Fiji plugin (2D, 2D+t):
  Plugins > StarDist > StarDist 2D
  https://imagej.net/StarDist
Tips:
  Read the documentation
  Nuclei appearance and size should be similar to training data (~20px)
For 3D: use python
Notes: Why doc? Powerful tool but important to know what it’s been intended for

## Slide 86: Advanced segmentation: CellPose
“CellPose”:
  a neural net for segmenting dense cells of a wide variety of shapes: nuclei and cytosols
Availability:
  Standalone GUI & python package (2D, 3D)
  For quick exploration: check out the website: http://www.cellpose.org/
Tips:
  Read the documentation

## Slide 87: Optional Exercise: StarDist, Cellpose
Segment a nuclei image with StarDist in Fiji. (AS_09125_050116000001_L15f00d0_slice1_channel1.tif)
Optional: Try segmentations at http://www.cellpose.org/