## Slide 1: Introduction to Image Analysis with FIJI
6. Image Registration, Tracking, and Stitching
Topics:
Image Registration
Time sequence analysis: Tracking
Image Stitching
Gayathri Nadar, Noreen Walker
Scientific Computing Facility, MPI-CBG
3.-7.5.2021
With material from:
Robert Haase
Benoit Lombardot

## Slide 2: Course schedule
Day 1 (Mon 3.5.)
  Image basics, visualization, measurements
  Spot detection
  Segmentation (start)
Day 2 (Tue 4.5.)
  Visit LMF
  Segmentation (cont’d)
  Mathematical background: image filters, morphology
Day 3 (Wed 5.5.)
  Advanced segmentation: Machine learning with Ilastik
  IJ Macro (start)
Day 4 (Thu 6.5.)
  IJ Macro (cont’d)
  3D data: visualization and analysis
Day 5 (Fri 7.5.)
  Image registration, image stitching
  Time sequence analysis and tracking
  Good practices

## Slide 3: Recap: 3D Visualization & Analysis
3D Data
Visualization
Analysis
Other tools
Anisotropy Required sampling
2D slicing
3D
3D segmentation and measurements

## Slide 4: Overview
Image registration
  Drift corrections in images
  StackReg tool in FIJI
Time sequence analysis
  Tracking
  Tracking in FIJI: TrackMate
Stitching
  Stitching tiles in FIJI: Grid-collection plugin

## Slide 5: Recap: Image dimensions
Images have up to 5 dimensions.
2D 3D (z-stack)
+ time + channels
A dataset can additionally consist of multiple tiles or views
Notes: Now we add time to our data!

## Slide 6
Image registration
x
y

## Slide 7: Motivation
Time lapse data is beneficial for many experiments
  Study how objects grow with time, e.g. embryo developments
  Tracking objects, e.g. cell migrations
Also comes with challenges
  Sample drifting
  Cells moving out of field
  Reduced signal with time
  …
Session goal: drift/motion correction in images
  Using image registration: fix a frame, “register” other frames to this
Drifting sample

## Slide 8: Image Registration
“Image registration is the process of transforming different sets of data into one coordinate system.”
Source: Wikipedia
x
x
Technically
  finding corresponding structures
  determining the optimal transformation to correct the misalignment of the images and
  apply the transformation
x
y

## Slide 9: Terminology
Most commonly, one image is moved/rotated/… to match it in the coordinate system of the other image.
x
y
Reference,
source or
fixed image
Target,
subject or
moving image

## Slide 10: Registration Strategies
Feature-based
versus
Intensity-based
Mean squared error of pixel values
MSE = 2000
MSE = 0
MSE = 1900
MSE = 500
System of linear equations
Optimisation

## Slide 11: Types of Misalignments
There are many facets of misalignments
The less we observe, the easier is the correction
aligned image
translation
rotation
scaling
shearing
isometric scaling

## Slide 12: Spatial Transformations
Translation only
Translation
+ Rotation
Rigid transformation
Translation
+ Rotation
+ Isometric scaling
Geometric similar transformation
Translation
+ Rotation
+ scaling
[+shearing]
Affine transformation
fixed
moving
Spatial transformations help to correct for the misalignments between fixed and the moving images
Notes: Today we look at translation = drift

## Slide 13: Quiz 1
By applying image registration from frame to frame, we can do drift correction.
Uncorrected
Corrected
Which transformation do we need to apply?
Translation
Rigid
Affine

## Slide 14: Registration: Many use cases
Registration appears in many image pre-processing steps, such as
Motion correction
Image source: http://www.zmescience.com/medicine/gifs-biology-human-body/
Original
Image source: https://svi.nl/ChromaticAberrationCorrector
Chromatic aberration correction
Slice alignment
Image source: http://imagej.net/Register_Virtual_Stack_Slices
Stitching
Image source: Carine Stapel (Vastenhouw lab)
Multiview reconstruction
Image source: https://fiji.sc/ Multiview-Reconstruction
Now we look at motion/drift correction
Later: Stitching

## Slide 15: Spatial Transformations: in Practice
These terms are variously used in registration software

## Slide 16: Registration in FIJI: StackReg Tool
Register a stack of image slices
  Slice visible or set by user = fixed image
  All the other slices in the stack = moving
Plugins > Registration > StackReg
http://bigwww.epfl.ch/thevenaz/stackreg/

## Slide 17: Demo/Hands-on: Drift Correction using StackReg
Open celegans_motion_correction.gif
Select a frame, where the investigated object is as centred as possible.
Plugins > Registration > StackReg

## Slide 18: Other Registration Tools in FIJI
Register Virtual Stack Slices
Ignacio Arganda-Carreras
FIJI plugin
Useful for big data
MultiStackReg
Brad Busse
FIJI plugin
Multichannel images

## Slide 19: Exercise: MultiStackReg
MultiStackReg allows you to register two stacks. For e.g. -
Register one channel to another
Exercise:
Open the image droplets_multistackreg.tif
Use slider to see the drift in action.
Duplicate the image
Split channels
Launch MultiStackReg plugin
  Plugins > Registration > MultiStackReg
Choose ch1 as Stack 1 and align ch2 to ch1
Select appropriate transformation
Merge channels
Compare with the original image
Tip:
Don’t forget to set the correct “reference” frame on Stack 1 (as with StackReg)
Image source: Basusree Ghosh (Tang lab)

## Slide 20
Time sequence analysis

## Slide 21: Time sequence analysis: Tracking
Tracking: ”following moving objects”
Active research field
  Algorithms
  Applications
High computational effort (complexity)
  High performance computing
Goals
  Measure track properties (speed, velocity)
  Study spatio-temporal relationships
  Single particle tracking
  Building cell lineages during development
Session goal: tracking objects in images
Source: Konrad Schindler, Computer Vision Lab, ETH Zuerich
http://www.vision.ee.ethz.ch/datasets/
Notes: Now we have corrected for drift, next -> track objects of interest and measure specific properties

## Slide 22: Tracking
Cell tracking in a nutshell
  Combines object detection and matching (or linking)
Steps
  Detect objects at all time frames
  Match/ link objects between consecutive time frames
Courtesy of Florian Jug, MPI CBG
Segmentation
t=1
Segmentation
t=2
matching
Segmentation
t=3
matching
Segmentation
matching
t-1
t
t+1
t-2
Assume 99% correct

## Slide 23: Tracking
Tracking needs many decisions.
Let’s assume we have:
  about 1000 objects
  500 time points (frames)
Number of decisions to be made – an approximation
  1000 + 499 * (1000+10002 ) = 499.500.000 (!!!)
More objects and timepoints -> more computationally expensive
Courtesy of Florian Jug, MPI CBG
Objects at
t = 1
Remaining
time pts
Objects to be matched
from t to t+1

## Slide 24: Tracking
Tracking errors propagate
  High accuracy at the beginning does not guarantee perfect output at the end
  As time points increase, the probability to err is high
t → t + 1: Assume 99% correct matching of objects
Time points: 100
  P(‘correct lineage’) ≈ 0.9999 ≈ 37%
Time points: 500
  P(‘correct lineage’) ≈ 0.99499 ≈ 0.07%
Courtesy of Florian Jug, MPI CBG

## Slide 25: Quiz 2
Tracking errors: Erroneous segmentation
  )
2
1
How many objects do you see?
Courtesy of Florian Jug, MPI CBG

## Slide 26: Tracking: Error Sources
Courtesy of Florian Jug, MPI CBG
  Missed objects (under-segmentation)
  Spurious objects (over-segmentation)
Erroneous segmentation

## Slide 27: Spot-detection: Track maxima
Alternative to segmentation; especially when tracking is the goal
The maxima finder algorithm uses a tolerance (minimum valley depth)
Tolerance: 120
Tolerance: 30
Tolerance: 15
In Fiji: Process > Find maxima…
Notes: In you are only interested in “track” properties like lifetime, velocity, etc. detecting maxima and tracking them should be enough

## Slide 28: Linking / matching
Linking (also “matching”) is the process of connecting spots to tracks by adding edges.
t
t+1
t+2
Courtesy of Florian Jug, MPI CBG
Linking is a linear assignment problem (LAP)
  Costs are associated for linking objects, merging tracks, splitting, etc.
  Optimized by solving for the solution with minimal costs

## Slide 29: Tracking Terminology
Lineage tree (“graph”)
“Track” (TrackMate)
“Edge” / “Link”
“Node” / “Spot” (Segments)
“Leaf”
“Root”

## Slide 30: Tracking Terminology
Spot detection + linking
Segmentation + matching
t
t + 1
t - 1
t
t + 1
t - 1

## Slide 31
Tracking in FIJI: TrackMate

## Slide 32: Tracking in FIJI: TrackMate
Go-to tool for tracking in FIJI
  Powerful
  Works with 2D and 3D data
  Maintained and well documented
  Macro/script support
  Active support on forum
Jean-Yves Tinevez

## Slide 33: TrackMate: Step-by-step
Reduce image data to the necessary by outlining an interesting area (1). The larger your file is, the longer the processing will take. Select a time range to reduce even further (2).
Image > Duplicate…
1
2
Loading tracking image data

## Slide 34: TrackMate: Step-by-step
Plugins > Tracking > TrackMate
1
Launch TrackMate

## Slide 35: TrackMate: Step-by-step
Configure blob diameter and threshold. Prefer “some to many” instead of “some missing”.
Difference-of-Gaussian based spot detection

## Slide 36: TrackMate: Step-by-step
In case there is a peak on the left of the quality diagram, put a threshold to exclude it. The less spots you continue to process, the faster tracking will work.
1

## Slide 37: TrackMate: Step-by-step
Use the time scroll bar to check various time points.
Finding the right parameters for all time points might be challenging.
1
2
3

## Slide 38: TrackMate: Step-by-step
If spot detection was wrong, consider going back to square one. Repeat all necessary steps.
2
1

## Slide 39: TrackMate: Step-by-step
Go through the following steps again. Repeat quality control.

## Slide 40: TrackMate: Step-by-step
Configure maximum distance for two spots (in subsequent time points) to be considered as the same spot. (1)
Define maximum distance between spots which are not present in subsequent time points (2)
The frame gap corresponds to the number of frames where the spot might not be present.
Use Fijis line tool to measure distances in the image (3/4).
1
2
3
4
Linking

## Slide 41: TrackMate: Step-by-step
Configure maximum distance for two spots to be considered as split event.
If merging is biologically reasonable, turn merging on.
1
2

## Slide 42: TrackMate: Step-by-step
Visualize track properties (1) to find regions (and time ranges) where something went wrong.
1
Visualize track properties

## Slide 43: TrackMate: Step-by-step
Add filters on tracks
  Using the + and – buttons
  Selector what to filter for
  Above/below choice
Inspect resulting tracks – why are there so little?
1
2
3
Filtering tracks

## Slide 44: TrackMate: Step-by-step
Use the TrackScheme (1) to visualize lineages. Are they reasonable?
1
Trackscheme

## Slide 45: Demo: TrackMate

## Slide 46
More tools/ plugins

## Slide 47: More tools for Tracking
MaMut
Jean-Vyes Tinevez
FIJI plugin for annotation of big-data
Mastodon
Tobias Pietzch (CSBD), Jean-Vyes Tinevez
Tracking in big-data
In-beta
ParticleTracker (MOSAIC SUITE)
MOSAIC Group, CSBD
FIJI plugin for tracking 2D/ 3D points
Notes: MaMuT itself does not ship any fully-automated or tracking algorithm. It is meant for manual or semi-automatic annotation. A semi-automated segmentation can help you generating quickly lineage branches from single cells.

## Slide 48: Add-on: Temporal color code
Fiji tool to color code objects with selected LUT over time
Great for visualization purposes
Input: 2D/ 3D time-series
Output:
1. RGB color-coded
2. Color scale
Image > Hyperstacks > Temporal Color-Code
https://imagej.net/Temporal-Color_Code

## Slide 49: Add-on: Bleaching Correction
Photo-bleaching: fluorescence decay from the samples with time
  Common issue with time-lapse data
  Resulting intensity measurements might not represent true values
In FIJI, Image > Adjust > Bleach Correction offers solutions for bleach correction
For details on the methods: https://f1000research.com/articles/9-1494
https://imagej.net/Bleach_Correction

## Slide 50: Summary
Registration
Tracking
x
y

## Slide 51
Exercises
Indicate in the online docx whether you are finished and if you need a live demo of difficult steps.

## Slide 52: Exercise: Track spots using TrackMate
Open SwimmingAlgae.tif
Launch TrackMate
Check if the calibration is correct!
Step 1: Blob detection
  Use the Log detector to detect spots
  Use line tool to measure spot diameter (median filter is useful to remove noise)
  Use preview!
  Hint: Check results in several frames
Goal: Tracking spots in SwimmingAlgae.tif and visualize trackscheme

## Slide 53: Exercise: Track spots using TrackMate
Step 2: Visualize spots
  Set filters if necessary to discard spurious spots
  Play around with the “set color by” option
Adding filters

## Slide 54: Exercise: Track spots using TrackMate
Step 3: Linking
  Use LAP Tracker
  Frame to frame linking max distance: maximum distance for two spots (in subsequent time points) to be considered as the same spot.
  Track segment gap closing: maximum distance between spots which are not present in subsequent time points
  Max frame gap: maximum number of consecutive frames where the spot might not be present
  Turn on splitting and merging only if biologically reasonable
  Bonus: Does Simple LAP Tracker also work for this data?

## Slide 55: Exercise: Track spots using TrackMate
Step 4: Visualize track properties
  Use track filters if needed
  See which properties affect which tracks

## Slide 56: Exercise: Track spots using TrackMate
Step 5: Visualize track scheme
  Do your tracks look reasonable?
    Clean up tracks by filtering them and check Trackscheme again
  Bonus: check out the Track Display mode
  Save as XML file!

## Slide 57: Exercise: Track spots using TrackMate
Bonus 1: Plot track properties
  Press Next on the display options window

## Slide 58: Exercise: Track spots using TrackMate
Bonus 2: Export image with tracks overlay
  Press Next from Plot Features window

## Slide 59
Image Stitching

## Slide 60: Recap: Image dimensions
Images have up to 5 dimensions.
2D 3D (z-stack)
+ time + channels
A dataset can additionally consist of multiple tiles or views
Notes: Now we add time to our data!

## Slide 61: Stitching
Samples are often too big to fit into a single field of view.
Then: Sample is acquired in tiles and must be stitched later.
Typical tile overlap: 10-15 %
Image source: Carine Stapel (Vastenhouw lab)

## Slide 62: Stitching
Stitching is an application of image registration.
Typical steps:
  Pre-align tiles based on acquisition pattern or meta-data.
  Compute shifts of overlapping tiles and optimize globally.
  Fuse the tiles.
Image source: Carine Stapel (Vastenhouw lab)

## Slide 63: Stitching in FIJI: Grid/Collection plugin
In Fiji: Plugins > Stitching > Grid/Collection Stitching
Define pre-alignment

## Slide 64: Grid/Collection plugin
Tile pattern
Input images
Do the shift computation
Display fused image

## Slide 65: Grid/Collection plugin
The plugin also stores a tile configuration file.
Save the fused image.

## Slide 66: Vignetting
Fused image are often patterned:
  Inhomogeneous illumination
  Bleaching at tile overlap
Correct tiles before stitching:
  Divide tiles by a flatfield image.
Ways to get a flatfield image:
  Fluorescent dye
  Average many blurred tiles
  Cidre / BaSiC Fiji plugins
Image source: James Cleland (Rink lab)
/
=

## Slide 67: Other stitching tools
BigStitcher (Fiji plugin)
  Use for big data of many GB and if Grid/Collection fails.
Imaris Stitcher
  Easy usage
Microscope acquisition software
https://imagej.net/BigStitcher#UI_Overview
https://imaris.oxinst.com/products/imaris-stitcher

## Slide 68: Demo: Stitching
Use the Grid/Collection plugin to stitch the sample data.
Notes: Snake by rows: right & down,
X=5,y=2, overlap=15%
Afterwards: show example of wrong pre-arrangement -> will fail totally

## Slide 69: Quiz 3: Stitching
Stitching of image tiles is an application of image registration.
What type of transformation is usually used for alignment?
Rotation
Translation
Affine

## Slide 70: Summary
Stitching tiles
Registration
Tracking
x
y